## Slide 1: Cache Memory

## Slide 2: Cache
small amount of fast memory
sits between normal main memory and CPU
may be located on CPU chip or module
word
transfer
block
transfer
cache
cache views main memory as organized in “blocks”
smaller than
main memory

## Slide 3: Cache
The purpose of cache memory is to speed up data accesses for processor by storing information in faster memory made of SRAM
The data stored in cache is data that the processor is likely to use in the very near future

## Slide 4: Locality of Reference
An implication of locality is that we can predict with reasonable accuracy what instructions and data a program will use in the near future based on its accesses in the recent past.
Temporal locality: a recently executed instruction is likely to be executed again soon
Spatial locality: instructions with addresses close to a
recently executed instruction are likely to be executed soon.

## Slide 5: Parameters of Cache memory
Cache Hit
  A referenced item is found in the cache by the processor
Cache Miss
  A referenced item is not present in the cache
Hit ratio
  Ratio of number of hits to total number of references => number of
hits/(number of hits + number of Miss)
Miss penalty
  Additional cycles required to serve the miss
  Time required for the cache miss depends on both the latency and
bandwidth
  Latency – time to retrieve the first word of the block
  Bandwidth – time to retrieve the rest of this block

## Slide 6
Yes
No

## Slide 7
Block Placement
Direct Mapping
Set Associative
Block Identification
Fully Associative
Tag
Index
Offset
Block Replacement
FCFS
LRU
Update Policies
Random
Write Through Write back
Write around
Write allocate
Cache Memory Management Techniques

## Slide 8: Example
V.Saritha@VIT University, SCSE

## Slide 11: Direct Mapping from Cache to Main Memory

## Slide 13: Direct Mapping
N-bit CPU memory address – k bits index field and (n-k) bits tag field
Index bits are used to access the cache.
Each word in cache consists of data word and its associated tag
On memory request, index field is used to access the cache.Tag field of CPU address is compared with the tag in the word read in the cache

## Slide 14: Operation
CPU generates a memory request with (TAG;INDEX)
- Access Cache using INDEX ; (tag; data)
Compare TAG and tag
- If matches -> Hit
Provide Cache[INDEX](data) to CPU
If not match -> Miss
-word is read from the memory
It is then stored in the cache together with the new tag replacing the previous value

## Slide 15
When memory is divided into blocks of words, index field – block field and word field
Ex: 512 words cache – 64 blocks of 8words each – block field (6bits) and words field (3bits)

## Slide 16
Tags within the block are same.
When a miss occurs, entire block is transferred from main memory to cache.
It is time consuming but improves hit ratio because of the sequential nature of programs.

## Slide 17: Direct Mapping pros & cons
Simple
Inexpensive
Fixed location for given block
  If a program accesses 2 blocks that map to the same line repeatedly, cache misses are very high

## Slide 18: Associative Mapping
Fastest, most flexible but very expensive
Any block location in cache can store any block in memory
Stores both the address and the content of the memory word
CPU address of 15 bits is placed in the argument register and the
associative memory is searched for a matching address
If found data is read and sent to the CPU else main memory is accessed.
CAM – content addressable memory

## Slide 19: Set-Associative Mapping
Each word of cache can store 2 or more words of memory under the same index address
The comparison logic is done by an associative search of the tags in the set similar to an associative memory search, thus the name “Set-Associative”

## Slide 20
Hit ratio increases as the set size increases but more complex comparison logic is required when number of bits in words of cache increases
When a miss occurs and set is full, one of tag-data items are replaced using block replacement policy

## Slide 21: Problems
A set associative cache consists of 64 lines or slots, divided into four line sets. Main memory consists 4k blocks of 128 words each. Show the format of main memory addresses.

## Slide 22: Performance analysis
Look through: The cache is checked first for a hit, and if a miss occurs then the access to main memory is started.
Look aside: access to main memory in parallel with the cache lookup;

## Slide 23
Look through
TA = TC + (1-h)*TM
TC is the average cache access time
TM is the average main memory access time TA is the average access time.
Look aside
TA = h*TC + (1-h)*TM
number of references found in the cache
hit ratio h =
total number of memory references
Miss Ratio m=(1-h)

## Slide 24
Example: Assume that a computer system employs a cache with an access time of 20ns and a main memory with a cycle time of 200ns. Suppose that the hit ratio for reads is 90%,
what would be the average access time for reads if the cache is a “look-
through”cache?
The average read access time (TA) = TC + (1-h)*TM
20ns + 0.10*200ns = 40ns
what would be the average access time for reads if the cache is a “look-Aside” cache?
The average read access time in this case (TA)
= h*TC + (1-h)*TM= 0.9*20ns + 0.10*200ns = 38ns

## Slide 25: Source of Cache misses
Compulsory Misses: (Cold start)
Occur when a program is first started
Cache does not contain any of program’s data yet
Capacity Misses:
Occurs because the cache has a limited size
  (Working set is larger than cache size )
  Solution: increase cache size
Conflict Misses:
.
  (One set fills up, but space in other cache sets )
  Solution : increase cache size

## Slide 26: Block Replacement
Least Recently Used: (LRU)
Replace that block in the set that has been in the cache
longest with no reference to it.
First Come First Out: (FIFO)
Replace that block in the set that has been in the cache
longest.
Least Frequently Used: (LFU)
Replace that block in the set that has experienced the fewest references

## Slide 27: Update policies
Write Through
Write Back
Write allocate
No write allocate (Write Around)

## Slide 28: Write through
Update main memory with every memory write operation
.
Advantage:
- easy to implement
  main memory always has the most current copy of the data (consistent)
Disadvantage:
  write is slower
  every write needs a main memory access
  as a result uses more memory bandwidth

## Slide 29: Write back
the information is written only to the block in the cache.The modified cache block is written to main memory only when it is replaced.
To reduce the frequency of writing back blocks on replacement, a dirty bit is commonly used. This status bit indicates whether the block is dirty (modified while in the cache) or clean (not modified). If it is clean the block is not written on a miss.
Advantage:
  writes occur at the speed of the cache memory
  multiple writes within a block require only one write to main memory
  as a result uses less memory bandwidth
Disadvantage:
    harder to implement
    main memory is not always consistent with cache

## Slide 30: Write allocate and Write around
Write-Around
  correspond to items not currently in the cache (i.e.
write misses)
  the item could be updated in main memory only without affecting the cache.
Write-Allocate
  update the item in main memory and bring the block containing the updated item into the cache.

## Slide 31: A two-way set associative cache has lines of 16 bytes and a total size of 8k bytes. The 64-Mbyte main memory is byte addressable. Show the format of main memory addresses.

## Slide 32: Problem 2
V.Saritha@VIT University, SCSE
A two-way set associative cache has lines of 16 bytes and a total size of 8k bytes. The 64-Mbyte main memory is byte addressable. Show the format of main memory addresses.

## Slide 33
Consider a memory system with Tc = 100ns and Tm = 1200ns. If the effective access time is 10% greater than the cache access time, what is the hit ratio H in look-through cache?
TA = TC + (1-h)*TM
1.1 Tc = Tc + (1-h)*TM
0.1TC = (1-h)* TM
0.1 * 100 = (1-h) *1200
1-h = 10/1200
h = 1190/1200

## Slide 34
A computer system employs a write-back cache with a 90% hit ratio for writes. The cache operates in "Look Through" and has a 80% read hit ratio. Reads account for 60% of all memory references and writes account for 40%.If the main memory cycle time is 300ns and the cache access time is 30ns, what would be the average access time for all references (reads as well as writes)?

## Slide 35: References
J. L. Hennessy & D.A. Patterson, Computer architecture: A quantitative approach, Fourth Edition, Morgan Kaufman, 2004.